## Slide 1: Introduction To Computer Subtraction Using Complements
Instructor:
Mohammad Hasan
B.Sc Engineering in CSE
Final Semester, Final Year.
Kryptonite Lab
Coding Flow

## Slide 2
Complements Come up in storing numbers in the computer
Complements also arise in the operation of subtraction
There are two types of complements
        1’s Complement
        2’s Complement
Introduction -

## Slide 3
Example-
Binary Number
1111 0000 1111
1’s Complement
0000 1111 0000
2’s Complement
1
+
0000 1111 0001

## Slide 4
Exercise I-
1 1 1 1 0 0 0 0
- 1 0 0 0 1 1 1 0
1’s
0 1 1 1 0 0 0 1
2’s
1
+
0
1
0
0
0
1
1
1
1 1 1 1 0 0 0 0
+ 0 1 1 1 0 0 1 0
0
1
0
0
0
1
0
1
1
Overflow
The Result is 0 1 1 0 0 0 1 0
1 0
Carry
Put in
1

## Slide 5
Exercise II-
1 1 0 0 . 0 1 1 0
- 0 0 1 0 . 1 0 0 0
1’s
1 1 0 1 . 0 1 1 1
2’s
1
+
1
0
1
0
0
1
1
0
1 1 0 0 . 0 1 1 0
+ 1 1 0 1 . 1 0 0 0
0
1
1
1
1
0
1
0
1
Overflow
The Result is 1001.1110
.
.
1
1
1
1
1

## Slide 6
Practice Session -
Find the 1’s complement and 2’s complement of the following numbers ?
    1110101
    111100111
Evaluate the following numbers ?
    10010 - 11011
    11101 - 1011
Answer
1’s = 0001010, 2’s =0001011
1’s = 000011000, 2’s = 000011001
Answer
1001
10010