## Slide 1: Introduction To Computer Primary Logic Gates
Instructor:
Mohammad Hasan
B.Sc Engineering in CSE
Final Semester, Final Year.
Kryptonite Lab
Coding Flow

## Slide 2
A logic gate is an electronic component that can be used to construct the circuit.
Primary Logic gates
OR Gate
AND Gate
NOT Gate

## Slide 3
Key Point of Logic Gates-
Truth Table
Symbol of the Gate
A truth table is a mathematical table used in logic—specifically in connection with Boolean algebra, Boolean functions, and propositional calculus

## Slide 4
How many rows in a truth table?
Depends on input numbers
If N input, then the number of rows will 2N
If 2 input, then the number of rows will 22 = 4

## Slide 5
OR Gate -
Input
Output
Symbol
A
Y = A + B
B
+
If 2 input, then the number of rows will 22 = 4
0
0
0
1
0
1
1
1
1
1
1
0
If all of the input is 0 then the output be 0 otherwise output is 1

## Slide 6
A
B
Y = A + B
OR Symbol

## Slide 7
AND Gate -
Input
Output
Symbol
A
Y = A . B
B
.
If 2 input, then the number of rows will 22 = 4
0
0
0
1
0
0
0
1
1
1
1
0
If all of the input is 1 then the output be 1 otherwise output is 0

## Slide 8
A
B
Y = A + B
AND Symbol

## Slide 9
NOT Gate -
A
Y = A
Input
Symbol
Output
It is an inverter operation, if input 0 then output 1 or if input is 1 then output is 0
0
1
1
0

## Slide 10
A
NOT Symbol
Y = A